## Slide 1: What Makes A Simulation Credible? Cost-Effective VV&A in the Systems Engineering Process
Focusing “V&V” on “A”
Notes: This briefing provides a short overview of the VV&A process used at the Naval Air Warfare Center, Aircraft Division (NAWC/AD) under the Naval Air Systems Command (NAVAIR).

## Slide 2: NAVAIR VV&A Process
NAVAIR VV&A Branch uses risk to determine how much and what kind of information is needed to support using models and simulations (M&S)
What is the risk to the decisionmaker if the M&S results are in error, but we use them anyway?
    What is the likelihood that the M&S is in error?
    How important is the decision?
    How much reliance are we placing on M&S results to make a decision?
We develop a risk matrix based on the answers to those questions
    Using Likelihood of Error and Consequence of Error ratings
    Based loosely on the system safety risk assessment process
  We identify mitigation actions to reduce the risk to an acceptable level
    Those mitigation actions form the basis for Accreditation and V&V Plans
    Don’t do any V&V that doesn’t directly reduce the risk of using the M&S!
Notes: The Naval Air Systems Command (NAVAIR) uses a risk-based process to evaluate the suitability of M&S to support system acquisition program goals. This cost-effective process has been developed, exercised and improved over the last 30 years for multiple programs.

## Slide 3
Verification: The process of determining that a model implementation and its associated data accurately represents the developer's conceptual description and specifications.
  Does the model do what the originator intended, and is it relatively error free?
Validation: The process of determining the degree to which a model and its associated data are an accurate representation of the real world from the perspective of the intended uses of the model.
  How well do model results match real world data, in the context of your needs?
Accreditation: The official certification [determination] that a model, simulation, or federation of models and simulations and its associated data are acceptable for use for a specific purpose.
  Does the accreditation authority have adequate evidence to be confident that a model is fit for purpose?
  Definitions from DODI 5000.61 dated 13 May 2003
Did you build the model right?
Did you build the right model?
Did your customer accept it as sufficiently credible to be “fit for purpose?”
What is M&S VV&A?
Notes: These are the official DOD definitions of verification, validation and accreditation. They were developed early in the 1990’s by the Military Operations Research Society (MORS) in a series of workshops and later codified in the DOD Dictionary (DODI 5000.61). Verification and validation are activities performed to collect information about model and simulation (M&S) credibility, and Accreditation is a decision that the M&S is suitable for a specific application, based on that V&V information and other information about the M&S (as we’ll see later in this tutorial).

## Slide 4
How is it “Measured”?
What is M&S “Credibility”?
How Does All This Relate to “VV&A”?
How Much Credibility is “Enough”?
?
M&S Credibility
Notes: The M&S User, who is faced with this challenge of demonstrating that a selected simulation has sufficient credibility for his or her purposes, first needs to understand the nature and scope of this challenge. Some of the questions that must be answered are shown here.
First it is fundamental that the term “M&S credibility” is clearly understood. What is the definition of the term and what elements contribute to credibility?
Second, the User needs to know how credibility is “measured” or quantified. How do the various elements contribute to the case for credibility? How can one tell if a particular simulation is credible?
Next, the User needs to know “how much credibility” is really needed. How many of these elements must be present to establish that he or she has sufficient credibility? What evidence is needed to demonstrate that each element is present to a sufficient degree?
Finally, the obvious question is how is credibility related to VV&A. Everyone is aware that VV&A is needed. But how does VV&A contribute to this case for credibility that is needed? Does one satisfy the need for credibility by doing VV&A?

## Slide 5
M&S User
It Depends on Risk
BUT
A Makeshift Bridge is Good Enough If You Need To Cross a Meandering Shallow Stream
M&S
PROBLEM
CREDIBLE
SOLUTION
How Much Credibility Is “Enough”?
Notes: In attempting to make an accreditation assessment, most evaluators face the common question of “how much of this V&V information is necessary to demonstrate credibility for a particular application?”. The answer to this questions depends in large part on risk. If the consequences of using an inaccurate simulation are not severe, the risk is relatively low, and one would not need much evidence of simulation credibility.
Just as in this picture, a makeshift structure of evidence may be satisfactory for low-risk applications.

## Slide 6
Indicate the Need for
Evidence of Greater Credibility
PROBLEM
CREDIBLE
SOLUTION
M&S
Supporting Evidence
Greater Risks...
Notes: However, in those cases where inaccurate simulation predictions could have disastrous consequences, one needs much more evidence to guarantee that the simulation is credible enough to reduce the risks. For example, the simulations that are being used to prove that the ballistic missile defense system will work under all circumstances must have a lot of credibility to justify the expenditure of funds on so large and important a system. The risks associated with erroneous performance predictions and a potentially inadequate missile umbrella would be extremely high. In these cases, the User should demand a comprehensive accreditation assessment that is supported by a strong foundation of extensive V&V results. In these situations, the case supporting the accreditation needs to be fully documented and reviewed.
The guiding principle is that quantity and quality of the evidence is directly related to the level of risk of the intended use.

## Slide 7
Most people think “Validation” (AKA “Output Accuracy”) is the hallmark of simulation credibility
  The degree to which simulation outputs match the “real world”
There are three ways to define the “Real World”
  Benchmarking – Another simulation with established credibility
  Face Validation – Subject Matter Expert (SME) expectations
  Results Validation – Test Data
But each of these have well-known limitations
  Uncertain benchmark simulation credibility
  Disagreements among SMEs
  Test data availability, limitations & cost
Fortunately, there are other measures of simulation credibility we can add to Validation
What Makes a Simulation “Credible”?
Notes: Output accuracy is the result of traditional model validation efforts. Output accuracy is defined as the degree to which simulation outputs match the real world under similar scenario conditions. It should be noted that no simulation will match the real world perfectly. Thus, output accuracy is really a relative term, and the User must determine if the “match” is good enough. To make this determination, the User must have some idea of how accurate he or she needs the outputs to be. Also, the comparison should be done under conditions and scenarios that match the intended use of the simulation. Thus, if a transportation simulation is being used to predict supply support in the Antarctic, validation results that rely on data collected in CONUS may not be appropriate.
Validation, by definition, is a comparison of simulation outputs with some representation of the real world. It is not always possible to collect data to be used in validating a simulation. In such cases, other means of representing the real world are used. These can include either other models that have been proven in some way and accepted as representative, or expert judgment that is based on extensive, real-world experience. In any case, some type of validation results are generally necessary to demonstrate output accuracy.
So “what makes a simulation credible?” In most M&S circles, people tend to look at validation results to determine if the simulation is any good.
Reliance on validation results as the primary indicator of credibility has several limitations and pitfalls. One of the primary limitations is that the simulation can only be validated at a few, very specific points. It is physically impossible to validate any simulation for all possible combinations of input conditions. If a simulation had some bug that only became apparent under certain specific sets of conditions, such a bug might not be found. Even if the simulation was validated for a set of conditions where the bug had an effect, the anomalies in the outputs may be attributed to other factors and the bug might not be detected.
Another limitation on using validation as the primary indicator of simulation credibility is the normal constraint on any budget. In most cases, collection of data for validation can be rather costly. It is impossible to collect data for a large number of validation cases. Furthermore, the real world usually has some factors that affect the data, yet these factors are not represented in the simulation. Thus, the data must be “scrubbed” to eliminate the effect of these factors. There may be some conditions where the impact of such factors may not be recognized; thus, the validation results may indicate a problem that really only reflects a modeling assumption.
Finally, wargames, simulations of conceptual systems, or other systems requiring validation data that cannot be measured are not amenable to standard validation methods. Typically, such simulations undergo face validation, a method with much less precision.
These factors lead one to look for other, complementary credibility indicators.

## Slide 8
V&V are Just the Middle of the Bridge!
Output Accuracy
Simulation meets design requirements, operates as designed and is free of errors in software
Software (S/W) Accuracy
Simulation input data, validation data and data manipulations are appropriate and accurate
Data Accuracy
Simulation outputs match the real world “well enough” to be of use in a particular problem
Validation
Verification
&
S/W Accuracy
Output Accuracy
Data Accuracy
"V"
"V"
V&V: The Central Pillars of Simulation Credibility
Notes: Approaching the question of what makes a simulation credible from an abstract perspective, one can think of a simulation as the bridge. To build confidence that the bridge is adequate, one would assess the capabilities and characteristics of the bridge in light of the requirements for the bridge. Typically, one would review and evaluate some combination of design information, engineering certifications, test reports, builder qualifications, maintenance records, etc. to determine if the bridge was adequate for the type and level of traffic that was expected. In an analogous way, we can assess the credibility of a simulation for a specific application based on knowledge of its design, the accuracy of its software (verification results), the accuracy of its outputs (validation or test results), the accuracy of its input data, its usage history, etc..
Most people think of simulation credibility in terms of three types of accuracy: software accuracy, data accuracy and output accuracy. Software accuracy refers to the error-freeness of software design and coding; data accuracy refers to the accuracy and appropriateness of input data to the simulation; output accuracy refers to the degree to which simulation outputs match the real world. These aspects of simulation credibility are easily recognized as the objects of verification and validation activities. These elements give one an understanding of simulation accuracy. However, these elements, alone, do not comprise a comprehensive assessment of simulation credibility!

## Slide 9
Simulation possesses all required functionality and fidelity for the problem being solved
Anchors the M&S to the Problem
Simulation has adequate user support to facilitate correct operation and interpretation of its outputs
Ties the M&S to a Useful Solution
Accuracy
M&S
Requirements
Capability
User
Capabilities
Usability
Problem
Credible
Solution
Capability
Usability
Can I Be Sure I’m Not Mis-Using the M&S?
M&S
Does the M&S Do What I Need It To Do?
How Accurate are:
  Software
  Data
  Output?
The “Other Pillars” of Simulation Credibility
Notes: Our experience suggests that simulation accuracy (as defined in the previous slide) is a necessary but not a sufficient condition for a robust determination of simulation credibility. The software may be demonstrably free of errors, the data may be demonstrably accurate and correct, and simulation outputs may correlate well with real world data. But does the simulation represent all the real-world phenomena that affect the problem you are trying to solve? Does it simulate these functions at the appropriate level of detail? Is the simulation (software, documentation and data) managed well? Is it accompanied by enough support structure to allow you to use it credibly, given the user’s level of experience with the simulation?
Questions like these provide the approaches to our simulation “bridge” and provide the linkage between the bridge and the anchor points on the banks of the river that must be crossed. Any robust assessment of simulation credibility must consider not only “accuracy”, but also “capability” and “usability” in determining whether it is suitable for use in a particular application. Any accreditation assessment that is evaluating simulation credibility for a given application must consider all five of these credibility elements.

## Slide 10
Credibility = f (Capability, Accuracy, Usability)
Capability
  Functional and Fidelity Characteristics
  Assumptions & Limitations
Accuracy
  Software, Data, Outputs
Usability
  Training, Documentation, User Support
  Appropriate Hardware & Software
V&V
The Simulation Credibility “Equation”
Notes: The purpose of the entire accreditation process and in particular the accreditation assessment is to demonstrate that the simulation has appropriate credibility for the intended application. It should be noted that this assessment does not add to or improve the basic credibility of the simulation which is built into it when it is developed. Rather the assessment merely defines and builds a case that demonstrates how much credibility the simulation has and whether that level of credibility is sufficient for the application.
When discussing credibility, we note that it can be viewed as some function of capability, accuracy, and usability. As noted on the chart, accuracy is broken down into types, namely software accuracy, data accuracy, and output accuracy. In an accreditation assessment, each of these elements of the credibility picture are evaluated separately to gain an understanding of the overall level of credibility.

## Slide 11
Without adequate evidence, you’re out on a limb using model results…
.
.
M&S
USER
Accreditation is a Decision
An official determination that a model, simulation or federation of simulations is credible enough and suitable for a specific application
Accrediting authority needs to provide justification for selection and use of a given simulation for a given problem to reduce program risk in using the M&S
Notes: The key to making VV&A activities fruitful is to focus on accreditation. According to official documents accreditation is an official determination that a model is acceptable for a specific purpose. In essence, a responsible official must make a judgment about model suitability and must be able to defend that judgment if challenged. The official normally charged with this responsibility for acquisition programs is the acquisition program manager, who is responsible for making the final decision based on the outputs of the M&S that are being accredited.
A defendable accreditation decision requires an assessment of evidence showing that the simulation is credible. This evidence is organized and presented so as to evaluate whether the simulation has sufficient capability, accuracy, and usability to satisfy the needs of the application.
If accreditation is based on such a comprehensive assessment, the program manger, or whoever else makes the accreditation decision, can have confidence that the risks associated with an incorrect decision are understood and mitigated.

## Slide 12
Evidence of capability, accuracy and usability gives you a solid base for confidence in model results
Capability & Usability Evidence
M & S
USER
V&V Evidence
Evidence Supporting Accreditation
V&V products provide essential information that contributes to simulation credibility
  Software, data and output accuracy
BUT V&V alone are insufficient to support accreditation
  Capability and Usability requirements must also be addressed
  DoD, Service, and Agency policies all require evidence of some aspects of capability and usability
Notes: An obvious question is where does one find the “evidence” is needed to make the accreditation assessment. Most of this evidence is generated through verification and validation activities.
  Verification - the process of determining that a model implementation accurately represents the developer's conceptual description and specifications. (That is, does your model do what you expect it to?)
  Validation - the process of determining the degree to which a model is an accurate representation of the real world from the perspective of the intended uses of the model. (That is, just how well does the model represent your problem?)
The documented simulation verification and validation results provide information about the model’s capabilities, limitations, accuracy, and attributes. Data V&V provides information about data accuracy and suitability. All this information provides the foundation on which the accreditation authority can build and defend his case to support model suitability.
Although V&V results are major inputs to an accreditation assessment, they are not the only inputs needed. Information about the model’s basic functioning, operations, and results processing can also be found in the model documentation, from usage history, and from other users. All this information provides the support for accreditation.

## Slide 13
TO DEMONSTRATE THE M&S IS SUITABLE FOR THE NEED
REQUIRES AN OBJECTIVE COMPARISON
OF M&S REQUIREMENTS WITH M&S INFORMATION
WITHIN THE CONTEXT OF THE PROBLEM
THAT IS ADEQUATELY DOCUMENTED
M&S CREDIBILITY
REQUIREMENTS
M&S CREDIBILITY
INFORMATION
IDENTIFY
WORK-AROUNDS,
USAGE CONSTRAINTS,
REQUIRED IMPROVEMENTS
AND RISKS
IDENTIFY
DEFICIENCIES
ACCREDITATION
DECISION
Capability
Accuracy
Usability
Data Quality
M&S Documentation
Design Documentation
Configuration Mgt
V&V Results
Etc.
Defined by the User
(Formally or Implied)
Provided by the Model Developer
and/or Model Proponent
PROBLEM CONTEXT
The Essence of Accreditation
Notes: It is important to understand just what accreditation entails. This diagram shows a simplified view of what accreditation really is and how it is typically done.
Within the DoD, accreditation is defined as the official determination that a model is acceptable for a specific purpose. In practical terms, this definition implies that accreditation depends on a comparison of a model’s capabilities, limitations, and attributes with the simulation requirements that are generated from the specific problem for which the model will be used. To make such a judgment about model suitability, one must have a complete set of simulation requirements. These requirements are derived from the unique problem which the User is trying to solve.
In addition to the simulation requirements, one must also have documented evidence of the simulation’s capabilities, limitations, and attributes. Typically, this information is found in the sources indicated. A key part of this information is the evidence of data quality. This evidence is quite frequently obtained from sources completely separated from the Model Manager.
In making the assessment, one usually cannot be satisfied with a simple “no” answer if the capability, accuracy, or usability of the simulation does not meet requirements. In these cases, one must analyze the impacts of any deficiencies, determine if any work-arounds exist, and evaluate these against the requirements. Such an analysis should yield a list of tasks that must be done to make the simulation acceptable for the particular application.

## Slide 14
V&V is a “rheostat” gradually shining light on the problem: how much light you need depends on the risks of using M&S results
If you need to stumble to the bathroom in the middle of the night:
  You only need a little light to keep from stubbing your toe on the dresser
If you need to shave before that big interview:
  You need more light to avoid cutting yourself
If you’re performing brain surgery:
  You need a lot of light to keep from killing someone!
If you’re developing system requirements:
  You may only need a little information to support M&S use early in the program
If you’re demonstrating specification compliance:
  You need to be pretty sure the M&S works right, so you don’t have to absorb redevelopment costs if it leads you to the wrong design
If you’re into Operational Test & Evaluation:
  You need to demonstrate and document that the M&S works right or the OTD may cancel your system as unsuitable or ineffective!
V&V is a Process – Accreditation is the Decision – Risk is the Metric
Notes: Think of V&V as a “rheostat”, gradually shining light on the credibility of the M&S, rather than an “on/off” switch where the M&S is either “validated” or it’s not. How much light is needed on the subject depends on what you intend to do with it. If you just need enough light to find your way to the bathroom in the middle of the night without stumbling over a chair, then a small amount of light is sufficient. If you are trying to shave once you get to the bathroom, then you’ll need more light to keep from cutting yourself. And if you’re trying to perform open-heart surgery (presumably somewhere other than your bathroom), then you need even more light to keep from killing somebody. Accreditation is the “decision” that there is enough light shed on the subject to determine if you can proceed according to plan, or if instead you need to revise your plan based on what you see: how much V&V information you need to support that decision is determined by a risk assessment. If your only risk is stubbing your toe, then you can get by with very little V&V data to support your use of the M&S; if your risk is cutting yourself right before your big job interview, then you’ll need more V&V data; if someone’s life is at risk, then you’ll need a lot of V&V data and other supporting information if you’re going to use the M&S for your application. Thus, our answer to the question “How much VV&A is enough?” is “It depends on how much risk the user is willing to accept!”

## Slide 15
Conduct Preliminary Risk Assessment
(Capability, Accuracy, Usability)
Develop Accreditation Plan
Develop V&V Plan
Write Accreditation Report and Make Recommendation
M&S Accreditation Decision
Develop Intended Use Statement and Articulate Program Requirements
VV&A Team Support
VV&A Team
Model User
Program Manager
Model Developer
Accreditation Authority
Subject Matter Experts
SME Support
Execute V&V Activities
Write V&V Report
Evidence Sufficient?
Conduct Risk Assessment
(Capability, Accuracy, Usability)
Update V&V Plan
SME Support
Yes
No
Prepare and Issue Accreditation Decision Letter
VV&A Team Support
SME Support
Prepare M&S Management Plan or M&S Support Plan
Develop M&S Requirements (Capability, Accuracy, Usability)
Review Accreditation Package
Define Acceptability Criteria and Metrics for the M&S Requirements
NAWCAD IBST Risk-Based VV&A Process
Notes: Think of V&V as a “rheostat”, gradually shining light on the credibility of the M&S, rather than an “on/off” switch where the M&S is either “validated” or it’s not. How much light is needed on the subject depends on what you intend to do with it. If you just need enough light to find your way to the bathroom in the middle of the night without stumbling over a chair, then a small amount of light is sufficient. If you are trying to shave once you get to the bathroom, then you’ll need more light to keep from cutting yourself. And if you’re trying to perform open-heart surgery (presumably somewhere other than your bathroom), then you need even more light to keep from killing somebody. Accreditation is the “decision” that there is enough light shed on the subject to determine if you can proceed according to plan, or if instead you need to revise your plan based on what you see: how much V&V information you need to support that decision is determined by a risk assessment. If your only risk is stubbing your toe, then you can get by with very little V&V data to support your use of the M&S; if your risk is cutting yourself right before your big job interview, then you’ll need more V&V data; if someone’s life is at risk, then you’ll need a lot of V&V data and other supporting information if you’re going to use the M&S for your application. Thus, our answer to the question “How much VV&A is enough?” is “It depends on how much risk the user is willing to accept!”

## Slide 16
The Intended Use Statement describes the questions you’re trying to answer and the problem you’re trying to solve
  Indicates specifically how M&S will contribute to the solution
  Developed through extended conversations between M&S developers, analysts and users
  Essential first step
M&S Requirements document the M&S characteristics necessary to be suitable for the intended use
  Functionality, fidelity, operating environment, input data, etc.
Acceptability Criteria and Metrics
  Define in detail how you’ll decide if the M&S meets your needs
Information Requirements document the information the decision maker needs in order to accept the M&S as credible and suitable
  Influenced by policy, personal experience, expert advice
Intended Use Statement
Notes: Development of an intended use statement by the user of M&S is an important step in the accreditation process. The intended use statement should be developed by an iterative approach between the M&S developers, the M&S users, and the analysts who will be using M&S outputs to support program decisions.
There are two types of requirements for the M&S that need to be satisfied: M&S requirements, which document the functionality and fidelity needed for the intended application, and Information requirements to document the justification for an accreditation decision.

## Slide 17
Focus V&V on M&S Intended Uses
?
A lot of money is misspent on V&V activities
Cost-effective V&V needs to focus on addressing:
  What questions do the users need to answer?
  What M&S outputs will be used to help answer those questions?
  What characteristics must the M&S have to provide those outputs?
      Capability, Accuracy, Usability
  What information is needed to show the M&S has those characteristics?
      V&V results, CM artifacts, documentation, pedigree, etc.
  What information is missing, and how can we best develop it?
  What are the risks of not obtaining that information?
V&V should be tied to intended uses through requirements
  Eliminate any M&S requirements that are not relevant to the specific intended use
VV&A Team may need to help the user derive:
  Detailed intended use statements
  Requirements tied to those uses
Ultimate Goal: Reduce the Risk of using M&S
  To an acceptable level for the intended use
Notes: The key to effective VV&A is to focus all V&V efforts on the intended use of the M&S. The intended use identifies specifically how the M&S will be used to support a decision, identifies the credibility requirements for that intended use, and informs an assessment of the risk of using the M&S based on the available credibility information. Usually, the accreditation team has to help the M&S user to create a detailed and specific intended use statement, since many times the user hasn’t thought through in detail exactly how M&S outputs will be used in the decision-making process.

## Slide 18
Example of A General Intended Use Statement (IUS)
Intended Use for Traffic Flow Model (TFM)*
The Traffic Flow Model (TFM) will simulate a standard 4-way intersection in order to provide analysis of traffic flow control and provide support for implementing improvements in redirecting congestion.
The TFM will be applied for the following uses:
  To estimate the performance level of current traffic control systems to efficiently dissipate high density traffic congestion.
  To simulate variations of traffic flow situations in a naval base environment.
  To determine the effect of altering traffic control systems.
  TFM will be further developed in the future with increased complexity and fidelity to represent the entire traffic system of PAX NAS.
* Created by NAVAIR 5.4 VV&A Team Employees and Interns as part of a study project on “How to Build a Credible Simulation”
Notes: The key to effective VV&A is to focus all V&V efforts on the intended use of the M&S. The intended use identifies specifically how the M&S will be used to support a decision, identifies the credibility requirements for that intended use, and informs an assessment of the risk of using the M&S based on the available credibility information. Usually, the accreditation team has to help the M&S user to create a detailed and specific intended use statement, since many times the user hasn’t thought through in detail exactly how M&S outputs will be used in the decision-making process.

## Slide 19
Specific Intended Uses for Traffic Flow Model (TFM)
Notes: The key to effective VV&A is to focus all V&V efforts on the intended use of the M&S. The intended use identifies specifically how the M&S will be used to support a decision, identifies the credibility requirements for that intended use, and informs an assessment of the risk of using the M&S based on the available credibility information. Usually, the accreditation team has to help the M&S user to create a detailed and specific intended use statement, since many times the user hasn’t thought through in detail exactly how M&S outputs will be used in the decision-making process.

## Slide 20
M&S Requirements, Acceptability Criteria, Metrics & Measures
M&S Credibility Requirements flow from the intended use
Does the M&S do what you need it to?
  What capability (functionality & fidelity) is required?
  How will you evaluate that?
How accurate do the results need to be?
  Software Accuracy (including verification results)
  Data Accuracy (input and embedded data V&V)
  Output Accuracy (validation results)
  How will you evaluate all of those?
What needs to be in place to ensure that it is used properly?
  Configuration Management, Documentation, User support
  How will you evaluate those?
Notes: M&S Credibility Requirements, acceptability criteria and metrics come from the specific intended use statement (SIUS) – that SIUS drives the answers to these questions and populates a matrix of requirements, criteria and metrics for each application of the M&S in the SIUS.

## Slide 21
M&S Requirements | Acceptability Criteria | Metrics/Measures
Capability: functional and fidelity characteristics required | Documented specific details of requirements for design and data, and appropriate output parameters | Review of requirements and design, complete documentation, outputs are appropriate to the need
Software Accuracy: S/W is adequately tested | Appropriate and documented S/W environment, testing and verification | Review of verification and testing results and S/W development environment
Data Accuracy: input and embedded data are appropriate and documented | Authoritative input data sources, documented data V&V, verified data transformations | Review and acceptance of documented data V&V and sources
Output Accuracy: outputs are of sufficient accuracy for the application | Dynamic behaviors are appropriate; compares to benchmarking, SME expectation and/or test data | Review and acceptance of validation results important to the intended use
Usability: processes and documentation are in place to ensure proper operation and interpretation of outputs | CM is adequate and demonstrated; users are appropriately trained and supported; documentation is adequate for use | Review and acceptance of documented processes and demonstration that they are being followed
M&S Requirements, Criteria and Metrics
Notes: This is a general description of M&S requirements, criteria and metrics – each of the rows in this table is expanded with details derived from the specific M&S application in the intended use statement.

## Slide 22
M&S Requirement | Acceptability Criteria | Metrics/Measures
A. Atmospherics |  | 
A1 Simulate turbulent environmental conditions using either the von Karman or the Dryden Formulas | A1 The M&S incorporates either the Von Karman or the Dryden form of turbulence model | A1 SME review of comparisons between the wind output data (aircraft velocity, etc.) from the selected turbulence model and the expected turbulence form (Von Karman or Dryden)
A2 Simulate the air vehicle response to varying levels of wind gusts | A2 The M&S incorporates an ability to induce varying strength gusts onto the air vehicle | A2 SME review comparing the wind output data (aircraft velocity, altitude, wind velocity, etc.) from the gust model with expected gust model results
B. Air Vehicle |  | 
B1 Simulate mass properties of the Air Vehicle | B1.1 The M&S accepts a mass properties database | B1.1 SME review of documentation describing the process to incorporate a mass properties database file
 | B1.2 Mass property parameters output from the M&S agree with the expected output according to the database model | B1.2.1 Verify that the mass property parameters output from the M&S agree with the expected output according to the database model B1.2.2 SME Review of documentation supporting the validation of the process used to create mass property database files (mass property model)
Specific Acceptability Criteria & Metrics 6-dof Example
Notes: Here is an example of part of a table of M&S requirements, acceptability criteria and metrics for a six-degree-of-freedom (6-dof) air vehicle flight simulation.

## Slide 23
  * ETOS is defined as the total time the mission area is covered by an aircraft on station, divided by the total coverage time required
It’s easy to look like you’re making progress if you don’t know where you’re going…
Example: V&V of M&S that predicts Effective Time-on-Station (ETOS)*
Issue: The program had an intended use statement but no M&S requirements: this created many issues with verification as well as with the software
The program office was changing requirements during M&S development
The developer and the program office had no consensus on M&S requirements
  A software requirements document serves as an agreement between the program office and the developer
No software design requirements document meant there were no testable requirements for verification
Solution: We worked with the developer to create software design requirements
These software design requirements were used as testable parameters to create an implementation test procedure
Each requirement was matched with corresponding test(s)
It’s Hard to Conduct V&V Without Requirements
Notes: An ETOS model development forms an example of how important detailed M&S requirements can be for a program. By working with the developer and the potential user we were able to develop sensible requirements that tied to the program’s intended uses of the model.

## Slide 24
The Initial Risk Assessment identifies information gaps, risks and guides the V&V Plan
M&S CREDIBILITY
REQUIREMENTS
INITIAL
M&S CREDIBILITY
INFORMATION
IDENTIFY
WORK-AROUNDS,
USAGE CONSTRAINTS,
REQUIRED IMPROVEMENTS
AND RISKS
IDENTIFY
DEFICIENCIES
Capability
Accuracy
Usability
Data Quality
M&S Documentation
Design Documentation
Configuration Mgt
V&V Results
Etc.
Defined by the User
(Formally or Implied)
Provided by the Model Developer
and/or Model Proponent
PROBLEM CONTEXT
Initial Risk Assessment
Notes: Once the requirements, acceptability criteria have been established, in concert with the agency/program intending to use the results of the M&S to support decisions, we conduct an initial risk assessment based on existing M&S information available from the model developer or the model proponent. This risk assessment then will guide the development of an accreditation plan and a V&V plan, based on gaps and risks identified.

## Slide 25
NAVAIR M&S Risk Assessment Process
Notes: The NAVAIR risk assessment process combines assessments of the likelihood of error with ratings for the level of reliance the program is placing on the M&S for a decision, and the level of importance of that decision, and then combining these factors into a risk assessment matrix similar to those used in systems safety assessments.

## Slide 26
Error Likelihood Assessment
Error Likelihood is based on assessment of ten characteristics:
Well defined Intended Use and Acceptability Criteria
Conceptual Model Validation
Model Fidelity assessment WRT intended use
Software Design Validation
Input and Embedded Data V&V
System/Software Verification
Output Validation
Documented and Demonstrated Configuration Management
Complete and up-to-date Documentation
User Support Functions
Notes: The likelihood of error is developed based on ten M&S credibility characteristics, with red/yellow/green ratings being assigned to each of the ten characteristics and combined into one overall likelihood rating.

## Slide 27
Error Consequence Assessment
Error consequence based on how much reliance is placed on M&S results for decision-making and how important the decision is to program objectives
Reliance level is based on how much information is available (other than the M&S) to support the decision:
  Will M&S be the ONLY source of information, or the primary method supplemented by other data, or a secondary method, used to supplement other data, or a supplementary method only?
Importance level is based on the level of program decision involved (ORD threshold, KPP resolution, etc.) and/or on importance levels as described in MIL-STD-882 (systems safety)
Notes: The consequence of an M&S error on decisionmaking is based on assessments of how much reliance is being placed on M&S results in making a decision, and how important the decision is to the program.

## Slide 28
Low
Moderate
High
1
2
3
4
5
1
2
3
4
5
Error Consequence
Error Likelihood
Reduce reliance on M&S results
Improve M&S Credibility
Risk = Likelihood x Impact
Risk Reduction
Strategies
V&V Results
Reducing the Risk of M&S Use
Notes: Risk is then determined by combining the likelihood of error rating with the consequence of error rating into this risk “cube”. The slide illustrates the two basic risk reduction approaches that can be taken for M&S use. Error consequence is made up of reliance and importance: we can’t really affect the importance of the decision, but if we reduce the reliance on M&S results, we move from right to left in the figure and lower the consequence of incorrect M&S results to the program (by making use of other information in addition to M&S results for decision-making, such as supplementing M&S results with test results). If we improve the credibility of the M&S, we move from top to bottom on the figure by reducing the likelihood of a wrong M&S result (e.g., by conducting V&V activities, SME reviews, improving or enhancing the M&S algorithms, improving M&S documentation, just to name a few methods – anything that improves the credibility of the M&S). Most programs consider both approaches in their risk reduction plans. If done properly, both approaches can also help identify areas of improvement needed for M&S capability, accuracy, and usability.

## Slide 29
Establish Risk Levels For Each Application
  Identify Risk Types
  Determine Impacts and Likelihoods
  Determine Risk Level
Determine Appropriate Information Products Needed based on risk
  AIRGuide = Accreditation Information Requirements Guide
  Helps prioritize V&V tasking based on an assessment of risk levels
    For Each Credibility Component (Capability, Accuracy, Usability)
  Greater Risk Levels Dictate More In-depth Information and more formal documentation
  Based on interviews with 40+ programs and refined over 25+ years of use
Determine Appropriate V&V Activity For Each Information Product and develop V&V Plan
VV&A Planning
Notes: The general process for determining what information is needed to establish credibility is to first determine the level of application risk. This is done by first identifying the types of risk, then quantifying their impacts and estimating their probabilities of occurrence, next determining the level of risk for each type, and finally determining the overall risk level for the application [which is equivalent to the highest risk level among each of the types].
Based on the level of application risk, the appropriate types of information required to establish simulation credibility are identified using the AIRGuide. Knowing what information is already available, the user can identify the gaps and plan the appropriate V&V activities to generate the missing information.

## Slide 30
Example from Accreditation Information Requirements Guide (AIRGuide)
AIRGuide covers M&S Capability, Accuracy & Usability Issues
AIRGuide requirements are based on interviews with 40+ DOD Programs
Correlating Risk with V&V Activities
Notes: An example of one section of the guide is shown here. The first column contains the fundamental question. In this case, the question deals with software accuracy.
The second column identifies the items or types of information that can be used to indicate or assess software accuracy such as S/W development plans, development resource descriptions, or development artifacts.
The third column lists typical sources for each of these types of information. In this example, only the typical sources for S/W verification results are shown.
The last three columns indicate the scope and depth of information that would be needed to establish sufficient confidence that the software is error-free for different levels of risk. Note that the entries are based on our subjective judgement. Users should modify this guide if they have a reasonable rationale for doing so.

## Slide 31
Capability:
  Functional breakdown and description of simulation
  Summary of assumptions, limitations and errors
Usability:
  Demonstration of the computer hardware and operating system suitability
  Evidence of proper interface and operation of pre- and post- processors
  Operator qualifications
  Analyst qualifications
  Availability of user support services
  Usage/accreditation history
(* From AIRGuide)
Accreditation Information Requirements* (for initial assessment of moderate risk)
Software (S/W) Accuracy:
  S/W development and maintenance process description
  S/W development and management resources description
  S/W development and management artifacts and documentation
  S/W verification results
  S/W Quality Assessment
Data Accuracy:
  Indications of data quality
  Indications of quality assurance in the data generation process
  Indications of data manipulation accuracy
Output Accuracy:
  Benchmarking Results
  Face Validation Results
  Results Validation Documentation
  Sensitivity Analysis Results
Notes: These are information requirements from the AIRGuide for a moderate risk application of the M&S: low-risk and high-risk applications each have their own set of requirements either added to or removed from this list.

## Slide 32
OK
ETOS M&S V&V Example
V&V began with ETOS M&S Version 1:
Verification test procedures were developed using the software requirements document we created
  Multiple errors were discovered and documented
Software Quality Assessment (SQA) was performed via manual code review
  Relatively small code
  Biggest issue was lack of objects
Subject Matter Expert (SME) Review was performed
  Verification errors were confirmed
  Sensitivity analyses were reviewed
  In general, SMEs agreed that M&S was realistic enough for the intended use if known errors were corrected
The developer addressed multiple errors (bugs)
  Developer can address software issues using the following justifications: User Error, Software Test Error, Software Requirements change, No Fix and Software Update
  All major bugs should be fixed through a software update. Non major bugs can become new assumptions, limitations or known issues
  V&V continued with ETOS M&S Version 2:
  Verification test procedure was used again
  Multiple new errors were discovered
  Corrected in Version 3
Notes: Continuing the ETOS example, the VV&A team supported the developer through several iterations of the model by updating the required accreditation information, until a version that satisfied the user’s requirements was finally achieved.

## Slide 33
It works best when everybody pulls together
Each team member brings different expertise:
  Developer knows the specific M&S
  V&V Team knows cost-effective V&V principles
  SME know the technical area
But they don’t always work and play well together
  Developer can get defensive about their M&S
  V&V Team can be perceived as hyper-critical
  SME can get stuck on, “I’d have done it this other way”
V&V Works best when:
  V&V Team objective is to help the M&S work for the user
  Developer recognizes the benefits of V&V improving the M&S
  SME make constructive suggestions based on review of sensitivity analyses and all V&V results
  All V&V activities focus on reducing the risk of using the M&S for the specific intended use
Effective V&V Calls for a Team Approach
Notes: VV&A involves a wide variety of skill sets, including detailed knowledge of the intended use and associated M&S requirements, detailed knowledge of the M&S, knowledge of the technical areas involved in the application, and knowledge of VV&A processes. So VV&A works best as a team effort between the M&S developer, the M&S user, outside SME, the V&V agent, and the Accreditation Agent.

## Slide 34
Accreditation
An Accreditation Decision is based upon an assessment
    Using information available from existing resources and the results of any new V&V, does the M&S meet the acceptability criteria for the application?
    What workarounds are needed for the application?
    Is there adequate supporting documentation?
    What is the residual risk remaining after all VV&A results are in?
The user, the program office and the M&S developers need to work in cooperation to develop a meaningful accreditation case
Notes: Accreditation is usually a team effort between the accreditation authority, the M&S developer, the accreditation agent, the V&V agent (if they are a different group), and the V&V team. All of the efforts are directed at determining and reducing the risk to the program from potential erroneous M&S results.

## Slide 35
M&S Requirement | Acceptability Criteria | Metrics/Measures | Assessment
A. Atmospherics |  |  | 
A1 Shall simulate turbulent environmental conditions using either the von Karman or the Dryden Formulas | A1 The M&S incorporates either the Von Karman or the Dryden form of turbulence model | A1 SME review of comparisons between the wind output data (aircraft velocity, etc.) from the selected turbulence model and the expected turbulence form (Von Karman or Dryden) | Inspection has been documented; SME review identified no issues from a flying quality perspective; turbulence is subjective, and SME are supportive of what’s in the model. Acceptable
A2 Shall simulate the Air Vehicle response to varying levels of wind gusts | A2 The M&S incorporates an ability to induce varying strength gusts onto the Air Vehicle | A2 SME review comparing the wind output data (aircraft velocity, altitude, wind velocity, etc.) from the gust model with expected gust model results | Government and contractor SME are in agreement on how to handle gusting for purposes of spec compliance: Acceptable
B. Air Vehicle |  |  | 
B1 Shall simulate mass properties of the Air Vehicle | B1.1 The M&S accepts a mass properties database | B1.1 SME review of documentation describing the process to incorporate a mass properties database file | Documentation meets the requirement per SME Review: Acceptable
 | B1.2 Mass property parameters output from the M&S agree with the expected output according to the database model | B1.2.1 Verify that the mass property parameters output from the M&S agree with the expected output according to the database model B1.2.2 SME Review of documentation supporting the validation of the process used to create mass property database files | The V&V Report provides a clear-cut example of how they match. The SMEs are comfortable with mass properties representations in documentation. One additional document should be added to the list of supporting references – to be provided. Acceptable
Specific Capability/Accuracy Assessment 6-dof Example (SME Review)
Notes: For this example, each acceptability criterion and its associated metrics were assessed based on the information available and the documented V&V results; any risk areas were noted, and workarounds were identified as needed.

## Slide 36
Example:
Effective Time on Station (ETOS) should increase monotonically with endurance
Sensitivity Analysis revealed a bug: M&S called vehicle back from sortie for scheduled maintenance, and re-launch would have been at night (deck closed for 12 hours); scheduled maintenance events should wait until sortie is completed
That bug had not been identified by other V&V activities
SME Reviews of Sensitivity Analyses Can Help Support the Accreditation Case (ETOS Example)
Have the experts tell you if the results look suspect
Notes: We have found that structured Subject Matter Expert (SME) reviews are a key element of developing and refining an accreditation case for M&S use. SME are asked to review all the information supporting an accreditation decision, and sensitivity analysis results are very useful in demonstrating whether the M&S behaves as expected. This example shows results of the model that predicts effective time on station (ETOS) for an aircraft: in this case the behavior of the M&S was not as expected, and the SME helped identify the source of the error.

## Slide 37
Summary
VV&A is a risk reduction/mitigation process
Accreditation means comparing your credibility requirements for a simulation with what information you can gather about it, and assessing the residual risk of using it
  Credibility = Capability, Accuracy, Usability
We’ve developed a cost-effective way to gather the information required to support an accreditation decision
  Focus V&V activities on the Intended Use
  Make maximum use of existing (although possibly undocumented) information
  Use SME reviews to assess and document overall M&S credibility related to the intended use
Notes: VV&A is a risk reduction and mitigation process with two “cardinal rules”:
  V&V activities must be driven by the requirements of the M&S intended uses
  V&V activities must be designed to reduce the risk of using the M&S for those intended purposes
V&V activities not focused on reducing the risk of specific M&S uses are wasting your time and your customers’ money
The Accreditation Authority must answer the question: “Do I know enough about how well the M&S works to use it with acceptable risk?” And the Accreditation Authority should turn to subject matter experts, including those outside the program, to help assess and document the available M&S credibility information.

## Slide 38: Backups

## Slide 39
DOCUMENT | AFI 16-1001 | ARMY AR 5-11 | SECNAVI 5200.40 | DRAFT SECNAVI 5200.40A | DODI 5000.61 | DMSO VV&A RPG | ARMY PAM 5-11
V&V PLAN |  | X |  | X |  | X | X
V&V REPORT | X | X | X | X | X | X | X
ACCREDITATION PLAN |  | X |  | X |  | X | X
ACCREDITATION REPORT | X | X | X | X | X | X | X
SIMULATION SUPPORT PLAN |  |  |  |  |  |  | X
METADATA TABLES |  |  |  |  |  | X | X
VV&A Documentation Requirements

## Slide 40
Funds the development, (or modification) and use of M&S for his specific application.
Has the most to lose if M&S results aren’t believable.
M&S USER
Simulation Proponent
Accreditation Authority
M&S
DEVELOPER
Typically works for the M&S Program Manager.
Builds the software.
Performs V&V activities.
M&S PROGRAM
MANAGER
Typically works for the M&S User
Manages the M&S development effort.
Ensures that the User’s M&S requirements are accurately
captured and implemented in software.
V&V AGENT
Typically works for the
M&S Program Manager
or the User
Ensures that M&S Developer plans, conducts and documents V&V activities appropriately.
Typically works in support of the M&S User.
Ensures that V&V and other evaluation efforts support accreditation of M&S for specific applications.
ACCREDITATION
AGENT
M&S “Points Of View”
Notes: In discussing simulation credibility, its important to recognize that people will have different views of the issues depending on their role. The principal roles are shown in this slide.
The M&S User is the beneficiary of simulation credibility and generally the sponsor of any work to demonstrate or improve credibility. If the User needs a new model, he or she pays for the development and the V&V efforts. The M&S User is the one who takes M&S outputs and uses them to support technical program decisions – the User is not necessarily the person who runs the M&S, but rather is the one who uses the outputs of the M&S. The M&S User is typically the person who accredits the M&S for use.
The M&S Program Manager oversees the development of the simulation. Once a simulation has been put in use, the duties of the M&S Program Manager are generally transferred to a Model Manager who is responsible for maintaining configuration control, updating the simulation as necessary, and supporting the various users.
The Model Developer is the person, activity, or contractor who actually designs the simulation, writes the code, tests the code, and documents both the simulation and the development process. The Developer works for the M&S Program Manager.
The V&V Agent plans and oversees the V&V activities. For new models, the V&V effort generally follows a standard set of structured tasks that parallel development. For legacy models, any V&V activities are generally focused on producing particular types or pieces of information that might be needed for the accreditation assessment.
The Accreditation Agent assists and guides the Users through the accreditation process. He or she oversees the accreditation process, assists in defining the simulation requirements as necessary, determines information requirements from the V&V Agent and Model Manager, plans and guides the assessment, and prepares the accreditation report. The AA should be fully conversant with the accreditation process.

## Slide 41
M&S User/Accreditation Authority
Responsibilities for VV&A:
  Define the intended use and resulting M&S requirements
  Define the information required to perform an assessment of a simulation for accreditation
  Perform final accreditation assessment and make accreditation decision
Frequent Weakness
  Lack of knowledge of policy and “reasonable” practice in VV&A
  Lack of technical knowledge necessary to develop meaningful and sufficient requirements for M&S
  Lack of experience and “gut feel” necessary to determine what kind of correlation one should reasonably expect to see between good test data and simulation predictions for parameters of interest
  VV&A is incidental to their major activities (e.g., planning and conducting an OT&E program)

## Slide 42
?
?
Accreditation Agent
Responsibilities for VV&A
  Work with user and developer to ensure that the ASP is sufficient to support a meaningful accreditation assessment for the application
  Facilitate communication between different communities
  Provide up-to-date information on current policy and best practice
  Provide insight into cost/benefit trade of various V&V and documentation activities
Frequent Weaknesses
  Lack of detailed understanding of specific technical areas relevant to the M&S or the particular application
  May overlook value of existing informal documentation
  May not have sufficient authority to task individuals or establish priority of V&V related work
  May lack knowledge of policy and standard practice within the agencies represented by the M&S developer, M&S proponent, and/or end user

## Slide 43
M&S Developer Responsibilities
Develop M&S in a professional, disciplined manner
  Maintain documentation of the M&S development
  Plan, execute and document V&V required to show that the M&S meets its original requirements
  Maintain effective configuration management
Support accreditation efforts by providing users with information
  Provide expertise on the characteristics of your M&S
  Assist in creation of an Accreditation Support Package (ASP)

## Slide 44
Frequent Weaknesses of M&S Developers
May have difficulty separating aspirations for the M&S from what finally evolved
May not have funding to do formal documentation
  M&S Features and Manuals
  V&V Activities
May not understand User’s application for the M&S
May be defensive about requests for objective evidence of the quality of his product
  There is often a perception of bias in defending the M&S even if the developer has a very even view

## Slide 45
How The Developer Can Help the User/Accreditation Authority
Develop a straw-man set of M&S requirements based on the intended use
Provide adequate documentation of V&V activities
  Even if informal
Offer suggestions on comparing simulation predictions with test data
  How close the correlation must be for a given application
  How close one can reasonably expect the correlation to be given the uncertainties of testing

## Slide 46
How the Developer Can Help the Accreditation Agent
Provide technical support
  You are the expert in the area
Show the agent your records and describe any V&V work done in the past
  And any local practices related to simulation development and V&V
Produce at least informal documentation of V&V activities as part of the development process

## Slide 47
What’s the Issue with Documentation?
Everybody DOES some V&V to convince themselves that their M&S works correctly
  But almost nobody writes it down
    In a well documented, retrievable fashion
    So they can convince someone else
  They may not think of what they’re doing as V&V
  Documentation is lower priority than completing the code
    And it isn’t as much fun
Accreditation decisions must be backed up by evidence
  It’s hard to do with no documented V&V record
  Can’t rely on corporate memory
    People forget, leave, move on to other projects, etc.
Documentation is time consuming and requires funding
  But documentation that doesn’t keep pace with development is worthless
Notes: Documentation is another area that often takes a back seat in M&S development, particularly for M&S that are developed internally by the government. If documentation is not up to date and complete, a potential user has less confidence in the M&S.

## Slide 48
V&V Documentation Doesn’t Need to Be Formal
Example: A Mission Effectiveness Model
Developer initially said he had done no V&V and had no configuration management (CM) process
  However, we rummaged thru his files and found informal test reports, PowerPoint briefings and notes describing software test results going back over 20 years
  He was able to trace versions throughout development, since he was the only developer and the principal user
We documented the results he had, added some V&V results of our own, and recommended a CM process that he implemented
  The ultimate user accredited the M&S based on that evidence
Notes: This example shows that not all documentation has to be formal: informal documentation is acceptable if it is retrievable, particularly for lower risk applications.

## Slide 49
How to Better Use Documentation You Already Have
Information that supports accreditation often already exists, but is not complete or retrievable
  Briefings, meetings, peer reviews, notes  Record Keeping
    Necessary accreditation documentation
Often can be created without too much effort
  Focus on Content, not appearance
  Note references on existing briefings
    Just hand-write them on the hardcopy if you have to
  Write down which version of the simulation each briefing relates to, and which version of the hardware (if you’re modeling a real system)
  Keep resumes of all team members
    Document Team Qualifications
Summarize in Accreditation Support Package (ASP)
Notes: Here are some tips on improving existing documentation without breaking the budget.

## Slide 50
Accreditation Support Package (ASP)
An Easy, Scalable, Consistent Approach to Credibility Documentation
  Information elements were selected from surveys of accreditation authorities
  And refined over more than 20 years of use
An unclassified (usually) compilation of the information most needed to support accreditation
  Organized around the three aspects of M&S credibility
    Capability, Accuracy, Usability
Notes: The ASP is one way to summarize capability, accuracy and usability information.

## Slide 51
Some M&S Information That Supports Accreditation
  Capability:
    Conceptual Model
    Software Design Specification
    Summary of Assumptions and Limitations
  Accuracy (S/W, Data, Output):
    S/W test plans & results
    V&V plans & results
    Sensitivity Analysis results
    Expert Review results
    Data V&V results
    CMMI information
  Usability:
    S/W documentation
    Evidence of effective configuration management
    User group minutes, support website, etc.
Notes: The lesson from this discussion is that the simulation Developer can ease the User’s burden by clearly documenting a simulation’s capabilities. The most useful document is a well-written Conceptual Model. The guidelines for what should be contained in a conceptual model are explained in the MSCO VV&V Recommended Practices Guide that is accessible on the web at www.MSCO.mil/vva/. The information in the conceptual model should be written in operational terms that the User can readily understand. Typically, the conceptual model will contain at least the elements listed in the slide.
Another document that is extremely useful in determining a simulation’s capabilities is the software specification. This document describes the detailed design in technical terms, but not programming language. Users can often gain an understanding of technical details of the simulation’s capabilities from this document. Often the design specification will also present structural or flow diagrams that explain how the simulation will be built. These are also quite useful.
In all cases, the information in these design documents is only useful if it is current or can be related in some way to the current version of the simulation. This points up the need for a good configuration management program that provides the basis for relating information in such documents to the latest version of the simulation. A good CM program will have provisions for updating the conceptual model as part of any simulation upgrades.